ΑΝΑΡΤΗΤΕΟ ΣΤΟ ΜΗΤΡΩΟ

| Ελληνική Δημοκρατία Νομός Ευβοίας Δ.Ο.Α.Π.ΠΕ.Χ. Ν.Π.Δ.Δ. Δήμου Χαλκιδέων ΦΑΡΜΑΚΙΔΟΥ 15, 34100 ΧΑΛΚΙΔΑ ΑΦΜ: 997592294 ΔΟΥ’ ΧΑΛΚΙΔΟΣ ΤΜΗΜΑ: Aθλησης | Χαλκίδα 6/10/2016 A.Π. : 4363 Προς: κάθε ενδιαφερόμενο |
| --- | --- |

ΠΡΟΣΚΛΗΣΗ

ΘΕΜΑ:ΑΠΟΣΤΟΛΗ ΟΙΚΟΝΟΜΙΚΗΣ ΠΡΟΣΦΟΡΑΣ

Παρακαλώ όπως αποστείλετε οικονομική προσφορά για την προμήθεια του κατωτέρω συστήματος παρακολούθησης στο κλειστό Γυμναστήριο «Τ. Καμπούρης» στην Κάνηθο :

Τεχνική περιγραφή για προμήθεια και εγκατάσταση συστήματος CCTV στο κλειστό Γυμναστήριο «Τ.Καμπούρης».

ΚΑΤΑΓΡΑΦΙΚΟ  ΤΕΜΑΧΙΟ 1

• Third-party network cameras supported
• Up to 16 Megapixels resolution recording
• Support 1-ch HDMI, 1-ch VGA, HMDI at up to 4K(3840x2160)

resolution

• 8/16-ch network cameras can be connected with
80M/160M incoming bandwidth
• Up to 2 SATA interfaces
• Plug & Play with up to 16 independent PoE network
interfaces
• Support dual-os to ensure high reliablility of system

running

•Support various VCA detection alarm and VCA search

•Support H.265/H.264/MPEG4 video formats

ΚΑΜΕΡΑ ΟΡΟΦΗΣ  ΤΕΜΑΧΙΑ 2

1/2.8’’ Progressive Scan CMOS
• 1920 x 1080
• 20X Optical Zoom 
• DWDR 
• 3D intelligent positioning function 
• Support Hik cloud P2P
• Up to 100m IR distance 
• 12VDC & POE(802.3at) power supply

ΚΑΜΕΡΑ ΟΡΟΦΗΣ  ΤΕΜΑΧΙΑ 4

Up to 5 megapixel high resolution

Full HD1080p video

Dual video streams

4mm fixed lens

3D Digital Noise Reduction

3-axis adjustment

DC12V & PoE

Support H.264+

Up to 30m IR range

IP66 weather-proof protection

Mobile Monitoring via cloud P2P or iVMS-4500

ΚΑΜΕΡΑ ΟΡΟΦΗΣ  ΤΕΜΑΧΙΑ 2

Up to 5 megapixel high resolution

Dual video streams

2.8mm/4mm/6mm fixed lens

Digital Wide Dynamic Range

3D Digital Noise Reduction

3-axis adjustment

Support on-board storage

DC12V & PoE (

Up to 30m IR range

IP66 weather-proof protection

IK10 impact protection

Reset button

-S: Audio/Alarm IO

Mobile Monitoring via EZVIZ P2P or iVMS-4500

ΚΑΜΕΡΑ ΤΟΙΧΟΥ  ΤΕΜΑΧΙΑ 6

Up to 5 megapixel high resolution

Digital Wide Dynamic Range

3D Digital Noise Reduction

Up to 30/50/80m IR range

IP66 weather-proof protection

REMOTE CONTROL  ΤΕΜΑΧΙΑ 1

• Ergonomic design with 800×480 LCD touch panel 
• Live view and playback of video on screen at up to 1080p resolution 
• 1-channel video decoding for local preview
• Video capture and recording to local U-flash disk
• Compatible with DVR/DVS, matrix, network camera/dome, PC-DVR, etc.
• Support 15 operators, and each user is allowed to operate 256 devices

ΒΑΣΗ ΚΑΜΕΡΑΣ  ΤΕΜΑΧΙΑ 2

Κατάλληλη για την εγκατάσταση των 2 PTZ καμερών DS-2DE4220IW-D

Εγκατάσταση περιφερειακού εξοπλισμού: UPS 1000VA/600W, ΚΑΜΠΙΝΑ Rack 7U, Router δικτύου, Monitor και υποσύστημα για την διασύνδεση των καμερών με το καταγραφικό.

Παρακαλούμε για την αποστολή προσφορών εντός 6 ημερών ( καταληκτική ημερομηνία 12-10-2016).

Ο  Προϊστάμενος Διεύθυνσης

Φώτιος Μ. Γκούνης

ΠΕ A’